# THERMAL2 User Manual and Quick Reference
## Foreword
The thermal2 suite of codes has been written starting in 2014 by Lorenzo Paulatto[1]. It is based on an initial set of internal codes written by Giorgia Fugallo1,[2] and Andrea Cepellotti[3], both have also participated to the development. The code contains contributions from Michele Lazzeri1 and Francesco Mauri1,[4], as well as some subroutines from the Quantum-ESPRESSO distribution. Other people who have participated to the code development include Raffaelo Bianco1, Ion Errea1,[5] and Nicola Marzari3.
[1] IMPMC – UMR 7590 – Université Pierre et Marie Curie, Paris 6 / CNRS / IRD / MNHN
[2] LSI – École Polytechnique – Université Paris Saclay
[3] THEOS – École polytechnique fédérale de Lausanne
[4] Università di Roma – La Sapienza
[5] University of the Basque Country (UPV/EHU) and Donostia International Physics Center (DIPC)
## Copyright
All the files are provided under the GPL license, v2 or newer and, when possible, under the CeCILL license. A single file nist_isotopes_db.f90 contains data from the National Institute of Standards and Technology.
## Citing
We would greatly appreciate if when using the thermal2 suite of codes you cite the following papers where the underlying theory is described in detail (see also page 29):
- L. Paulatto, F. Mauri, and M. Lazzeri, Phys. Rev. B 87, 214303 (2013)
- G. Fugallo, M. Lazzeri, L. Paulatto, and F. Mauri", Phys. Rev. B 88, 045430 (2013)
- A. Cepellotti, G. Fugallo, L. Paulatto, M. Lazzeri, F. Mauri, N. Marzari, Nat. Comm. 6 (2015)
- G. Fugallo, A. Cepellotti, L. Paulatto, M. Lazzeri, N. Marzari, F. Mauri, Nano Letters 14 (11), 6109-6114 (2014)

## Quick Reference Manual
### Compiling the code
The thermal2 codes come bundled with the D3Q code, used to compute ab-initio the 3rd order dynamical matrices. We refer you to the D3Q manual for more detailed instruction on compiling. A separate stand-alone distribution of the thermal2 codes is being considered and may be available in the future.
### List of codes
The thermal2 suite of codes contains a number of small specialized codes that only take command line arguments, and a few larger codes that read input from a file. This is the list of codes and a brief description.

#### Main codes
Each of these codes will be reviewed in detail in a separate section.
##### d3_lw.x
This code computes several quantities:
1. phonon linewidth (i.e. its inverse lifetime, or HWHM, or minus the Imaginary part of the bubble-diagram self energy),
2. the entire bubble-diagram self energy (comprising both the linewidth and the lineshift) and
3. the phonon spectral weight for a range of energies.
It always includes the intrinsic anharmonic contribution from phonon-phonon interaction and can optionally include Casimir border scattering and isotope scattering.
##### d3_tk.x
The tk code computes the thermal conductivity. It can use the Single-Mode Approximation (SMA) or the variational approaches implemented by Fugallo et.al. [2] using a robust conjugate gradient minimization. It can include Casimir and isotope scattering.
##### d3_r2q.x
This code can compute the phonon frequency at a q-point or along a path, it can optionally print out the dynamical matrix. It is analogous to the matdyn.x code of the Quantum-ESPRESSO (QE) Phonon suite, but it uses the highly optimized subroutines developed for d3_lw.x and d3_tk.x. It should be used to check the phonon dispersion before doing more serious calculations.
#### Utilities
##### d3_q2r.x
This code is analogous to the q2r.x code of QE and it uses the same input, but produces a file of Force Constants (FCs) which has already been re-centered in the reciprocal space Wigner-Seitz cell to make Fourier Interpolation faster.
##### d3_qq2rr.x
Analogous to q2r.x but operates on the 3rd order matrices. This codes takes as command line arguments the dimension of the q-points grid and optionally the name of the output file. You must feed it feed by standard input the list of anharmonic dynamical matrices in the XML format produced by d3q.x. For example, d3q was run with fild3dyn=”anh” for a NQX x NQY x NQZ grid, you can compute the 3rd order Fcs as:
ls anh* | qq2rr.x NQX NQY NQZ [-o mat3R] [-f NFAR] [-w]
The result will be written by default to a file called mat3R, but you can change this with the -o option.
You can specify the optional argument NFAR (default=2) which is the number of neighbors that the code will scan to build the Wigner-Seitz cell. The default value usually works, you can set it to zero to avoid any re-centering: The resulting force constant will be unsuitable for doing any further calculation, due to aliasing in the Fourier interpolation, but they may be easier to import in another code.
The code will automatically select from the list the files that it needs to fill the grid; all the other files will be discarded. Which means that you can easily compute the force constants for any sub-lattice of the one compute, just by changing the values of NQX, NQY and NQZ.
After writing the force constant to file, the code will perform two optional tests (you can skip them pressing CTRL-C). First test: for this test the initial D3 matrices will be recomputed using the force constants with both the real and imaginary parts (which should be zero). Second test: recompute the D3 matrices with only the real part of the force constants. If any discrepancy is detected it will be printed on output. Notice that any discrepancy in the first test indicate a very serious problem with the D3 calculation. On the other hand, some discrepancy is inevitable in the second test; especially if you your atoms where not in the theoretical equilibrium positions. Also, increasing the cutoff and k-points can improve the consistency of the second test.
If the -w option is specified, when performing the FFT test, if the re-computed D3 matrix differs significantly from the initial one it will be printed to a file. The file will start with prefix 'anh_cmplx' for the first test and 'anh_real' for the second test.
##### d3_sparse.x
This code converts a file of third order FCs from dense form to sparse form; it can optionally discard elements that are smaller than a custom threshold. It can also measure the speedup gained by using the sparse FCs instead of the dense ones.
Syntax:
sparse.x [-i mat3R.input] [-o mat3R.output]
   [-t threshold] [-n num_trials]
Where ma3R.input (default mat3R) is the name of the dense file of Fcs, mat3R.output will be the output file of sparse FCs (you can use “none” to avoid saving them to file); threshold is in Rydberg/bohr3 (all matrix elements smaller than this will be discarded, default: zero, do not discard anything) and num_trials is the number of random trial q-point triplets to compute by Fourier interpolation. If num_trials is provided, the code will print out the elapsed time using the dense and sparse algorithm, the speedup and the eventual discrepancy between the two methods (which should be zero if the threshold is zero)
##### d3_asr3.x
This code applies the acoustic sum rules (ASR) to the third order FCs. It can only work on dense Fcs, not on the sparse ones. As the sum is applied iteratively, it will automatically stop after 10,000 iterations, or when the residual violation of the ASR is less than 10-12 or if a file named STOP is created in the running directory.
Syntax:
asr3.x [-i mat3R.input] [-o mat3R.output]
      [-t threshold] [-n iter_max]
This syntax will read the dense Fcs from file mat3R.input, apply the ASR iteratively until threshold is reached (default 10-12), or for iter_max, then save it to mat3R.output (default: mat3R.input.asr). If a file named “STOP” is found in the working directory, the code will stop after the next iteration and immediately save the Fcs to mat3R.output
##### d3_recenter.x
NOTE: this code is experimental and while useful for debugging, use at your own risk.
d3_recenter.x NQX NQY NQZ [-n NFAR]
        [-i mat3R.input] [-o mat3R.output] [-w]
Reads force constants from mat3R.input, interpolate them on a grid of NQX x NQY x NQZ points, recenter them on a Wigner-Seitz cell constructed up to NFAR unit cells and save the result in mat3R.input.recenter.
Uses the properties of Fourier interpolation to transform the 3rd order force constants from a grid to another. If the new grid is different than the initial one, some interpolation will be done, if the grid is the same, you can use the nfar parameter to recalculate the Wigner-Seitz cell centering. This code be useful to compare the results from grids of different sizes, or to put the force constants in a format that is easier to understand for external codes.
If the -w option is specified, the intermediate D3 matrices will, for the NQX x NQY x NQZ grid will be written to files called atmp_Q1*_Q2*_Q3*.
##### d3_import3py.x
d3_import3py.x NQX NQY NQZ [-n NFAR] [-w] [-s mat2R]
        [-i FORCE_CONSTANT_THIRD] [-o mat3R.3py]
Reads the force constants produced by Mingo & Carrete code thirdorder.py[6] and import them to the thermal2 format. The size of the supercell used for the FCs calculation must be specified as NQX x NQY x NQZ. In order to prepare the FCs for Fourier interpolation, they are taken to reciprocal space and then back to real space, and re-centered including up to NFAR neighbouring cell to ensure locality.
[6] http://www.shengbte.org/announcements/thirdorderpyv096
In order to read the system information (cell and position of the atoms) a file containing the force constants header in the thermal2 format must be provided with the -s option (default: mat2R). Note that a 2nd order FCs file, produced with d3_q2r.x or even with normal q2r.x, for the same system, is sufficient.
If the -w option is specified, the intermediate D3 matrices, generated on the NQX x NQY x NQZ grid, will be written to files with names atmp_Q1*_Q2*_Q3* (check the manual of d3q for details on the file names).
##### d3_sqom.x
NOTE: this code is experimental and currently not maintained, use at your own risk.
This codes reads a spectral weight file from d3_lw.x and computes the convolution with a Lorentzian function that has an energy-dependent FWHM. This procedures simulates the broadening introduced by Raman spectroscopy experiments. This code can also sum and average the spectral function coming from several different files, to simulate the uncertainty of the neutron wavevectors. It reads its input from a file called input.SQOM. Please see the code of PROGRAM_sqom.f90 for details.
##### funcoft.sh
This is a short bash script to get a plottable file of the linewidth of a specific phonon mode as a function of temperature.
It reads a list of linewidth files produced by d3_lw.x and extracts the frequency, linewidth (and if possible shifted frequency) from all files for a specific phonon q-point and band and prints a list ordered by temperature and smearing. Syntax:
  funcoft.sh point mode file [file2 [file3...]]
- point: index of the point to collect among the files
- mode: number of the phonon mode 1...3*nat
The output will contain 5 columns:
1. temperature
2. smearing
3. omega
4. linewidth (gamma, HWHM)
5. shifted frequency (if available in the file)
This script is provided “as is”, using non-standard names for the output files can break it.
##### diffd3.x
Compare two D3 files, write on output the matrix elements and the maximum difference. Take as arguments either two file names (the first and second D3 matrix) or two directory names a file name, which will be opened in both directories.
##### d3_sc2c.x
Open two D3 files, the first for a unit cell calculation for an arbitrary triplet, the second for a supercell calculation for a triplet of kind (0,q,-q). Then it refold the super-cell D3 matrix to the unit cell and compares the two.
##### xml2giorgia.x
Reads a list of D3 matrix files in XML format from standard input and write them to a single ASCII file called d3.txt
##### apply_asr.sh
apply_asr.sh [-i FILDYN.in] [-o FILDYN.out] [-a ASR_TYPE]
A simple bash script that applies the sum rule to a set of dynamical matrix files (FILDYN.in*, default: dyn) produced by phonon and saves them with a different name (FILDYN.out*, default: asr_dyn). Useful to apply the sum rule ‘crystal’ (default for ASR_TYPE) which is not supported by the thermal2 codes yet. The final fildyn files can be used normally with d3_q2r.x or q2r.x.
## Codes input and output
### d3_r2q.x
This code reads the 2nd order FCs and computes a number of different quantities that only depend on the harmonic 2nd order force constants, it is currently evolving and should be quite easy to modify and extend according to your needs.
It reads its input from a Fortran namelist called &r2qinput which contains the variables listed in the next section.
After the namelist, the code will look for the keyword QPOINTS and will start reading the list of q-points. This part is described in detail in section QPOINTS
#### Namelist &r2qinput
##### calculation (CHARACTER, default: “freq”)
The type of calculation to perform, currently this can be:
- "freq": Compute the phonon frequencies, this keyword that you specify nq and a QPOINTS section.
- "jdos": Compute the joint density of state. You will have to specify the integration grid nk and a configuration in the CONFIGS section (if you specify more, only the first configuration will be used)
- "rms" : Compute the root mean square displacement of the atoms around their equilibrium positions in the harmonic hamiltonian at a give temperature. It requires nk and one single configuration in CONFIG.
- "fh": Compute the phonon free energy or, for T=0, the zero-point energy.
##### prefix (CHARACTER, default: the value of calculation)
The first part of the output file name, the file will be called “prefix.out”.
##### outdir (CHARACTER, default: “./”, I.e. the current directory)
Location where the output file will be saved.
##### file_mat2 (CHARACTER, no default)
The file of the 2nd order force constants, produced by thermal2 internal version of q2r.x
##### asr2 (CHARACTER, default: “no”)
Method used to apply the acoustic sum rule, can be “no” (do not apply ASR), “simple” (apply the compensation term to the on-site force constant) or “spread” (distribute the compensation on all the FCs proportionally to their amplitude)
##### nq (INTEGER, no default)
Number of q-points to read (see the QPOINTS section below)
##### print_dynmat (LOGICAL, default: .false.)
If set to .true. A file containing the dynamical matrix, in phonon format, will be saved for each q-point (only works for calculation="freq"). The file name will be “r2q_dyn_NQ” where NQ is the progressive number of the point.
##### print_velocity (LOGICAL, default: .false.)
If set to .true. a file containing the phonon group velocities will be saved (only applies when calculation="freq"). The file name will be prefix_vel.out, after the path length and the q-point, the velocities are printed in Cartesian coordinates, Rydberg units (1.09×106 m·s−1).
##### ne, de, e0 (INTEGER, REAL, REAL, in cm-1 no default)
Used for jdos calculation, see the description in &lwinput section, below.
#### Output format
The r2q.x code will produce an output file for every configuration. The output files will be named $prefix.out (where $prefix is the value of the input variable prefix). It contains the following columns:
1.	A progressive integer number
2.	The length of the q-point path or, if computing over a grid the weight of the q-points
3→5.	The coordinates of the q-point in units of 2π/alat
6→5+3*nat.
The phonon frequencies in cm-1.
### d3_lw.x
This code can compute the intrinsic phonon-phonon interaction and the interaction of phonons with isotopic disorder and border scattering. It reads its input variables from the &lwinput namelist and from the QPOINTS, CONFIGS and ISOTOPES lists, which are described in detail in their corresponding sections.
#### Namelist &lwinput
##### calculation (CHARACTER, default: “lw”)
The type of calculation to perform, it can take several different values:
- “lw imag” : compute the imaginary part of the self-energy, i.e. the phonon linewidth. In this mode the code will enforce conservation of energy with a Diract delta function approximated with a Gaussian function of width delta, read from the CONFIGS section.
- “lw full” : compute the entire self energy, the real part is the lineshift and the imaginary part is the linewidth. In this case the value of delta from the CONFIGS will be used as a regularization for the self-energy.
- “spf full” : compute the spectra function for a list of arbitrary enegies, provided by the input variables ne, de and e0 (see below)
- “spf simple” : simulate the spectral function as a superposition of Lorentzian functions centered around the phonon frequencies and appropriate width, see also ne, de and n0.
- “final” (EXPERIMENTAL: be ready to look in the code to use this feature) : decompose the linewidth at a specific energy and q-point (specified with the q_initial keyword) over the energy of the final states in the scattering process or over the final q.
  in the first case you must specify the range of final energies to consider with the ne, de and e0 keywords; in the other case the final q-points will be read from the QPOINTS section, using a regular grid is recommended
##### prefix (CHARACTER, default: the value of calculation)
The first part of the output file name, the file will be called “prefix.out”.
##### outdir (CHARACTER, default: “./”, i.e. the current directory)
Location where the output file will be saved.
##### file_mat2 (CHARACTER, no default)
The file of the 2nd order force constants, produced by thermal2 internal version of q2r.x
##### file_mat3 (CHARACTER, no default)
The file of the 3rd order force constants, produced by qq2rr.x or asr3.x or sparse.x
##### asr2 (CHARACTER, default: “no”)
Method used to apply the acoustic sum rule, can be “no” (do not apply ASR), “simple” (apply the compensation term to the on-site force constant) or “spread” (distribute the compensation on all the FCs proportionally to their amplitude)
##### nq (INTEGER, no default)
Number of q-points to read (see below)
##### nconf (INTEGER, no default)
Number of configurations to read in the CONFIGS section, see the detailed description below.
##### nk (3x INTEGER, no default)
The size of the grid used to integrate the phonon-phonon interaction processes.
##### grid_type (CHARACTER, default: “simple”)
Set this to “simple” to use a regular unshifted grid in reciprocal space.
Use "random" to use a grid shifted by a random vector; the random shift is not applied to the directions where there is only one k-point, i.e. if you have a NxMx1 grid, there will be no shift along z. Furthermore, in a CGP calculation the shift applied to the inner and outer grid will be the same, while in all other calculations, they will be independent. Using a random shifted grid, can easily reduce the number of points required for convergence by half in each direction, for a speed-up of 8 for linewidth calculations and 64 times for tk calculations; however, it will break symmetry, and give (slightly) different thermal conductivity for different directions, even in highly symmetric crystals. See also xk0 to manually apply a grid shift.
Set to “bz” to use a grid centered in the Brillouin zone. This option will duplicate the points that are on the boundary of the BZ and assign them an appropriate integration weight. Using a BZ grid should eliminate a possible source of unwanted symmetry breaking, although it adds some complexity, uses more points, and its effectiveness is not evident in practice. It can be useful for doing plots. We recommend using “simple” instead of “bz”, unless you have some specific reason.
##### xk0 (3x REAL, default: 0,0,0)
A shift to apply to the grid of k-points, in units of half the lattice spacing; i.e. set it to (1,1,1) to have the Monkhorst-Pack shifted grid, any fractional values is allowed.
##### ne, de, e0 (INTEGER, REAL, REAL, in cm-1 no default)
When doing a Spectral function (d3_lw.x) or Final state (d3_lw.x ) or Joint-DOS (d3_r2q.x) calculation you have to define an energy axis with these variables. The axis will include ne equally spaced points starting from e0 and up to e0+ne*de.
##### e_initial (in cm-1, no default)
When doing a Final state decomposition calculation, this is the energy of the initial state considered in the scattering process. If you want to consider a specific phonon mode, just enter its energy by hand, in cm-1.
##### q_initial (3x REAL, in units of 2π/alat)
As e_initial, specifies the initial q-point.
##### q_resolved (LOGICAL, default: false)
When doing a Final state calculation Set to true to decompose the contributions to the linewidth over the q-points of the final phonons.
In this case, only one q-point can be specified in the QPOINTS section, using more points can have unpredictable results! The final state is decomposed over the grid of q-points used to compute the linewidth, i.e. the grid specified by nk.
##### sigmaq (REAL, default: 0.1 in units of 2π/alat)
Used in conjunction with q_resolved to obtain a nice smooth plot over the q-points by convoluting it with a Gaussian function of width sigmaq. Set it to something of the order of the spacing between the q-points.
##### exp_t_factor (LOGICAL, default: false)
UNTESTED/EXPERIMENTAL! When doing a spectra function calculation, add an elastic peak of equation (1 + f_bose(e,T)) / e) which should emulate the elastic peak of neutron spectroscopy.
##### sort_freq (CHARACTER, default: "default")
When plotting the linewidth and frequencies along a path, there are several ways to order the frequencies and associated linewidth and shifted frequencies:
- "default": keep the default order of increasing frequencies
- "overlap": sort each point in order to maximize the overlap of each band polarization with the corresponding band at the previous point. This is the best choice for paths, but probably will not work for 2D or 3D grid plots
- "shifted": sort in order of shifted frequencies, i.e. frequency+lineshift. It is only meaningful when doing a "lw full" calculation, it can help to have good quality plots when "overlap" fails.
##### isotopic_disorder (LOGICAL, default: false)
Set this to true to include scattering from isotopic disorder. You will also have to specify the isotopic composition of every element in the system in the ISOTOPES section. NOTE: isotopes are only used for linewidth calculation, they are no used for spectral functions and final state decomposition.
##### casimir_scattering (LOGICAL, default: false)
Set this variable to true to include scattering with boundary, treated with the Casimir formula. See the following variables for detail on how to specify the boundary structure. Casimi scattering is only applied to linewidth calculation, it has no effect on spectra function and final state calculations.
##### casimir_dir (3x REAL, normalized, default: no direction)
The direction in which Casimir scattering is prevalent. Set it to zero to consider omnidirectional scattering, i.e. scattering from grains, or to a specific direction to consider a wire. More complex geometries are not implemented yet, please let us know if you are interested.
##### casimir_length_au (REAL, bohr, no default)
##### casimir_length_mu (REAL, micrometers, no default)
##### casimir_length_mm (REAL, millimeters, no default)
The average scattering length in the Casimir model; you can specify only one of the three variables, according to the unit of measure you prefer. Note that the Caimir model also include a structure factor, usually set to 2, which is not included in our implementation; you will have to include it directly in the gain size in input.
##### max_seconds (no default, in seconds) max_time (format hh.mmss)
The maximum running time after which the code will stop, you can only set one of the two. Notice that only tk.x includes a restart mechanism.
#### Output format
The lw.x code will produce an output file for every configuration. The output files will be named
$prefix_T$XX_s$YY.out
Where $XX is the temperature in Kelvin and $YY the delta in cm-1. Each output file will contain a relatively large number of columns, depending on the calculation.
NOTE: In all of the following cases case when specifying QPOINTS as “grid” or “bz”, the length of the path will actually be replaced by the weight of the point used to do an integral in reciprocal space.
##### Calculation “lw imag”
Number of the column, or columns and its and content:
1.	A progressive integer number
2.	The length of the q-point path (when doing a path)
or the weight of the q-point (when doing a grid calculation)
3-5.	The coordinates of the q-point.
6→5+3*nat.	The unperturbed phonon frequencies in cm-1
6+3*nat→5+6*nat.
The linewidth (HWHM) in cm-1
##### Calculation “lw full”:
1→5+6*nat.	Same content as “lw imag”
6+6*nat→5+8*nat.
The shifted phonon frequencies (i.e. frequency+shift) in cm-1. If the sort_shifted_q keyword was set to true, the shifted frequencies are sorted in increasing order and the corresponding linewidth are sorted accordingly. The unperturbed frequencies are left unchanged.
##### Calculation “spf”:
1.	The energy axis in cm-1
2.	The length of the q-point path (when doing a path)
or the weight of the q-point (when doing a grid calculation)
3.	The total spectral function in 1/cm-1
4→3+3*nat.	Contribution to the spectral function from each band in 1/cm-1
Note that the energy axis cycles faster than the path length and there is a whitespace after each q-point which makes plotting with gnuplot “pm3d” style easy with this syntax (column 3 is used twice, both for heigth and colour):
sp “file” u 1:2:3:3 w pm3d
##### Calculation “final”, q_resolved FALSE:
1.	The energy axis in cm-1
2.	The total spectral function in 1/cm-1
3→2+3*nat.	Contribution to the spectral function from each band in 1/cm-1
Same as the spectral function, but instead of the spectra function there is the relative contribution of the specific energy to that point. QPOINTS are ignored in this kind of calculation, hence there is not path length.
##### Calculation “final”, q_resolved TRUE:
Same as the spectral function, but instead of the SPF you have the relative contribution of the specific energy at that point. The contribution to the linewith of q_initial will be assigned to every entry of QPOINTS by integrating the total contribution to the linewidth convoluted with a Gaussian of width sigmaq centered around it. In order to have the contribution from each of the points specified by the nk grid, set QPOINTS to generate the same grid. i.e.
QPOINTS grid
nk(1) nk(2) nk(3)
### d3_tk.x
The d3_tk.x code can compute the thermal conductivity coefficient in the SMA or by exact diagonalization of the BTE. Most of its input variables are the same as d3_lw.x, we refer to the previous section for their description
#### Namelist &tkinput
Most of the variable used by d3_tk.x are also used for d3_lw.x. The following variables have the same meaning as in d3_lw.x:
outdir, prefix, file_mat2, file_mat3, asr2, nconf, nk, grid_type, xk0, isotopic_disorder, casimir_scattering, casimir_direction, casimir_length_*
The following variables are specific of d3_tk.x.
##### calculation (CHARACTER, default: “sma”)
Set this variable to “sma” to compute use the single mode approximation or to “cgp” to do an iterative diagonalization of the BTE with the Conjugate Gradient algorithm with preconditioning. Please note that “cgp” algorithm will also output the SMA thermal conductivity at its first iteration, but computed in a slightly different way which is slower but guarantees the phonon-phonon scattering matrix to be well defined and the functional to be minimized to be positive definite.
Note that isotopic_disorder and casimir_scattering are properly implemented in for both SMA and CGP calculations.
##### nk_in (3x INTEGER, default: same value as nk)
When doing a “sma” calculation, the linewidth will be computed, for each point in the nk grid, integrating over the nk_in grid. Thermal conductivity will then be integrated over the nk grid. In principle, there is no reason for the two grids to be identical, as one quantity could be harder to converge than the other. When doing a CGP calculation, the inner and outer grids must be identical, nk_in will be ignored and nk used instead.
##### grid_type_in (CHARACTER, default: same value as grid_type)
Same as grid_type, but applied to the inner grid. Ignored for ‘cgp’ calculations.
##### xk0_in (3x REAL, default: same value as xk0)
Same as xk0, but applied to the inner grid. Ignored for ‘cgp’ calculations.
##### thr_tk (REAL, default: 1.d-4 W/mK)
Threshold on the convergence of thermal conductivity the of the CGP minimization when solving the BTE. The default value should be enough to get the thermal conductivity with 4 or 5 significant digits.
##### niter_max (INTEGER, default: 1000)
Maximum number of iteration of the CGP algorithm. Normally less than 100 iterations are needed.
##### restart (LOGICAL, default: .false.)
Set this to true, when doing a CGP calculation, and the code will write to disk the state of the minimization at each iteration, it will then be able to restart from the last step. Set this to .false. will have two effects: 1) the code will ignore any restart information already present on disk and 2) the code will not write restart information on disk. Restart information can take quite a bit of space for dense grids.
#### Output format
##### SMA calculation
When doing a SMA calculation the tk.x code will produce two output files:
1. A file named $prefix.$grid_size.out, where $prefix is the input value of prefix and $grid_size is the size of the integration grid (e.g. “20x20x20”). This file will contain one line per configuration, containing 1) the configuration number, 2) the value of sigma 3) the temperature 4-6) the diagonal elements of the thermal conductivity Kxx, Kyy and Kzz 7-12) The off-diagonal elements of K, in this order: Kxy, Kyz, Kyz , Kyx, Kzx, Kzy.
2. A file named lw.$prefix.$grid_size.out, same meaning as above, which contains a list of the q-points and the linewidth for each point and band.
##### CGP calculation
When a CGP calculation several files are created: one with the results at the last iterations for all the configurations and one file for each configurations with the results at each iteration. The thermal conductivity K is always in W/(m·K).
1. A file named $prefix.$grid_size.out, where $prefix is the input value of prefix and $grid_size is the size of the integration grid (e.g. “20x20x20”). This file will contain with the results from the last completed iteration of the code, one line per configuration, containing 1) the configuration number, 2) the value of sigma 3) the temperature 4-6) the diagonal elements of the thermal conductivity Kxx, Kyy and Kzz 7-12) The off-diagonal elements of K, in this order: Kxy, Kyz, Kyz , Kyx, Kzx, Kzy.
2. A file for every input configuration, named $prefix.$grid_size_s$XX_T$YY.out, where $XX is the smearing in cm-1 and $YY is the temperature in Kelvin. A line is appended to each file at each iteration containing: 1) the number of the iteration, 2) the value of sigma 3) the temperature 4-6) the diagonal elements of the thermal conductivity Kxx, Kyy and Kzz 7-12) The off-diagonal elements of K, in this order: Kxy, Kyz, Kyz , Kyx, Kzx, Kzy.
### QPOINTS
The “QPOINTS” card instruct the code to start reading a list of nq q-points, nq has been previously entered in the namelist. On the same line as QPOINTS thre optional keywords can be present:
##### cartesian (DEFAULT)
The points will be specified on Cartesian axis in units of 2π/alat, where alat is the lattice parameter. This is the default behavior of the code and is equivalent to not specifying any keyword.
##### crystal
The points are going to be specified on the basis of the reciprocal lattice vectors.
In the default, “cartesian” and “crystal” cases, the code will now start reading the q-points, one per line. After the q-point cooordinates, each line can optionally include an integer number, np, which instructs the code to make a straight path from the previous point to this one formed by np+1 points.
The code will also compute the total length of the path along the q-points. This length is printed in the output file (usually, 2nd column) and is useful for plotting.
You can use the special value -1 for np, to reset the length of the path at a certain point. The d3_lw.x code will also perform a special action depending on the context:
- When doing a linewidth calculation: print an empty line (useful for gnuplot 3D plots).
- When doing a spectra function calculation: continue writing to a new output file, which will have “_pN” appended to its name; N is a number increasing at each path reset.
If two consecutive points in the list are equivalent minus a G-vector, and if the latter has no np, or np=1, then the two points are added to the list with the same path length. This allows one to jump between equivalent point without having a discontinuity in the plot.
Another special value is the special value np=0 skips the point, but puts in in the list as null "previous point". I.e. the path will continue from the next point, as if the null point was the previous one. This allows to introduce a discontinuity in the path without resetting the length.
##### grid
Only used by the lw.x code when the calculation type is “grid”. On the next line the code will try to read three integer numbers, NQX, NQY and NQZ, which will define the dimension of the grid.
##### bz
Equivalent to “grid” but the grid will be translated in the Brillouin zone (i.e. the Wigner-Seitz cell of the reciprocal lattice), points on the boundaries will be duplicated to all the equivalent ones.
If you specify grid or bz, you can add, on the same line, a vector by which the grid will be shifted. The vector is in units of hals the grid spacing, i.e. a value of 1 indicates the standard Monkhorst-Pack shift, you can use any value.
#### Examples
Select the Γ point (000) and the X point (001) in a cubic lattice:
QPOINTS
2
0.0 0.0 0.0
0.0 0.0 1.0
Make a path K→ Γ → M in a hexagonal lattice, the path will include a total of 41 points:
QPOINTS
3
0.0 0.33333 0.33333
0.0 0.0 0.0 20
0.0 0.0 0.5 20
Make a line K→ Γ and then M→ Γ (in a hexagonal lattice), the path will include a total of 82 points:
QPOINTS
4
0.0 0.33333 0.33333
0.0 0.0 0.0 20
0.0 0.0 0.5 0
0.0 0.0 0.0 20
Make a 10 x 10 x 10 points grid
QPOINTS grid
10 10 10
Make a 10 x 10 x 1 points grid, shifted in the plane 10 x 10, but not along the third direction.
QPOINTS grid 1 1 0
10 10 1
Make three parallel lines of 101 points each, reset the path length after each line
QPOINTS
6
0 0 0
0 0 1 100
0 0.1 0 -1
0 0.1 1 00
0 0.2 0 -1
0 0.2 1 100
### CONFIGS
The “CONFIGS” card instructs the code to start reading a list of sigma (in cm-1)/temperature (in K) configurations. Sigma can be the width of a Gaussian smearing or the regularization of the self-energy, depending on the type of calculation. Configurations can be specified as a list (default), or as a matrix. In the former case a simple list is expected; in the latter case the code reads two lists: one of sigma and one of T and generates all possible couples.
##### list
If you specify "CONFIGS list" or just "CONFIGS", the number of configurations "nconf" is expected on the next line (deprecated: you can also use the nconf variable in the namelist). Afterwards, the code will read nconf lines, and expects a couple "sigma T" on each line. If on a certain line only one number is present, the code assumes it to be a temperature and it reuses the previous value of the delta.
##### matrix
After "CONFIGS matrix" the code will scan for the keyword "T" ("sigma"), followed, on the same line, by the number of temperatures (sigmas), the default value of 1 is taken if missing. The code will the read, on the following lines, the required values of temperature (sigma). See also the example below.
#### Examples
Select three configurations of increasing values of sigma and temperature:
CONFIGS
3
1.0 100
2.0 200
3.0 300
Select five different temperatures, all with the same smearing of 1cm-1:
CONFIGS
5
1.0	0
100
200
300
400
Build thirty configurations, from 10 values of temperature (K) and 3 smearings (cm-1):
CONFIGS matrix
 T 10
10. 20. 50. 100. 200.
300. 400. 500. 750. 1000.
sigma 3
2.
3.
4.
### ISOTOPES
After this car the code will read the information about the isotopic composition of all elements present in the calculation. This list will only be read if “isotopic_disorder” is set to true in the namelist.
Each element, identified by its name, must appear in the same order as in the file of the force constants. The isotopic composition can be specified in several different ways.
An isotopically pure element can be specified either by atomic number of the isotope or by setting manually its mass in atomic mass units (i.e. mass of 12C=12):
##### Xx N natm
Where Xx is the name of the element (e.g., H, Na, Cl), “N” is a keyword and natm is the atomic number
##### Xx M matm
Where Xx is the name of the element (e.g., H, Na, Cl), “M” is a keyword and matm is the atomic mass
If you wish to use the natural isotope concentration for an element you can use the following syntax:
##### Xx natural
Where Xx is the name of the element and “natural” is a keyword. The natural isotope concentration is stored in the file nist_isotopes_db.f90 of the thermal2 distribution. It is obtained from the NIST online database, available on the NIST website[7].
[7] http://physics.nist.gov/cgi-bin/Compositions/stand_alone.pl
If you wish to set the isotope concentration by hand you can use the following syntax
##### Xx isotopes niso
 m1 c1
…
mniso cniso
Where Xx is the name of the element, “isotopes” is a keyword and niso is the number of isotopes. You will then list the mass and concentration of each isotopes, on niso separate lines.
Finally, you can also specify directly the average mass for the element and its variance, which are the only two quantities that are actually used in the linewidth and thermal conductivity calculation. You can use the following syntax:
##### Xx manual gm gs
Where Xx is the element name, “manual” is a keyword, gm is the average mass and gs is its variance (both in Dalton units).
#### Examples
In the following example we will set Hydrogen isotopic concentration to 1) pure one-proton H 2) pure Deuterium 3) 50% H and 50% D 4) Hydrogen natural concentration 5) set gm and gs manually
H N 1
H M 2.01410178
H isotopes 2
1.00000000 0.5
2.01410178 0.5
H natural
H manual 1.02 0.01
## Input Examples
In the next sections you will find some example input files for the main codes of thermal2. You will find more examples, included a
### d3_lw.x
#### Computing the linewidth of a single point
This example input would compute the linewidth of q-point (1/3 1/3 0) in crystal (aka fractional) coordinates for 15 different values of temperature.
&lwinput
calculation = 'lw real'
prefix="lw_rnozp"
! file_mat2 = '../1l.FILDYN/mat2R.120ry.4.nozeu'
file_mat2 = '../FILDYN/mat2R.8_nozeu'
file_mat3 = '../FILD3DYN/mat3R.xxx_asr15_sparse'
outdir = './'
asr2 = 'simple'
nconf = 15
nk = 200,200,1
nq = 1
sort_shifted_freq = .false.
/
CONFIGS
2.0 0
      10
      50
      100
      150
      200
      250
      300
      350
      400
      500
      600
      700
      800
      900
QPOINTS crystal
0.33333333333 0.333333333333 0.0
#### Testing convergence with smearing and grid
The following example is useful for testing the convergence of the linewidth calculation as a function of the smearing value. The input should be run several times replacing NK with increasing values. You can then collect the linewidth of a band and plot a curve for every smearing as a function of the grid size.
&lwinput
calculation = 'lw imag'
prefix = 'lw_NK'
file_mat2 = '../FILDYN/mat2R.100Ry.4'
file_mat3 = '../FILD3DYN/mat3R_asr_sparse'
outdir = './'
asr2 = 'spread'
nconf = 7
nk = NK, NK, NK
nq = 1
sort_shifted_freq = .false.
/
CONFIGS
0.1 300
0.2 300
0.5 300
1.0 300
2.0 300
5.0 300
10.0 300
QPOINTS
0 0 0
You can then extract the data with a script like this:
#!/bin/bash
for smr in 0.1 0.2 0.5 1.0 2.0 5.0 10.0;do
grep "^ *1 " lw_*s${smr}.out|\
awk '{print $1,$(NF-2),$(NF-1),$NF}'|\
sed -re 's/lw_|_T|_s|.out|:/ /g' |\
sort -k 1n > s${smr}.dat;
done
And proceed to plot the curves included in the files s0.1.dat … s10.0.dat, e.g. with gnuplot.
You see that larger values of smearing converge with smaller grids but not to exactly the same value as smaller smearing. Using a smearing of the same order of magnitude as the average linewidth of the acoustic band is a good idea as the smearing can be identified with the intrinsic uncertainty of the phonon energy. An ideal procedure would use the actual linewidth for the smearing, but this should be done iteratively which would be much more computationally expensive. This scheme may eventually be implemented in the code if there is enough request.
In brief: do not take a value too small for the smearing, something of the order of a cm-1 is usually fine.
#### Compute the linewidth along a path in the BZ
&lwinput
calculation = 'lw full'
file_mat2 = 'mat2R'
file_mat3 = 'mat3R.xxx_asr_sparse'
outdir = './'
asr2 = 'spread'
nconf = 15
nk = 100,100,10
nq = 5
sort_shifted_freq = .true.
/
CONFIGS
5.0 0
      10
      50
      100
      150
      200
      250
      300
      350
      400
      500
      600
      700
      800
      900
QPOINTS
0 0 0
0.5 0.0 0.0 100
0.33333333333 0.333333333333 0.0 74
0.0 0.0 0.0 94
0.0 0.0 0.5 25
#### Compute the spectral function along a path
Spectral function calculations are not as well optimized as linewidth ones and can be much more memory intensive. If you are running out of memory, do not use more configuration that necessary, especially if running on massive parallel machines such as IBM BlueGENE.
&lwinput
calculation = 'spf'
file_mat2 = 'mat2R'
file_mat3 = 'mat3R.xxx_asr_sparse'
outdir = './'
asr2 = 'spread'
nconf = 1
nk = 100,100,10
nq = 5
 ne = 500
de = 1.0
/
CONFIGS
5.0 300
QPOINTS
0 0 0
0.5 0.0 0.0 100
0.33333333333 0.333333333333 0.0 74
0.0 0.0 0.0 94
0.0 0.0 0.5 25
You can obtain a color plot like those of ref. 5 with this gnuplot script:
set log cb
splot 'spf_full_T300_s0.3.out' u 1:2:3 w image
#### Compute the final state decomposition
&lwinput
calculation = 'final'
file_mat2 = 'T_295K/mat2R'
file_mat3 = '../mat3R_asr'
outdir = 'T_295K/'
asr2 = "simple"
nconf = 3
nk = 20, 20, 20
nq = 1 ! actually unused
e_initial = 490.80
q_initial = -0.5, 0.0, 0.0
ne =201
de = 3.5
e0 = 0.
/
CONFIGS
5 295
10 295
20 295
QPOINTS
0.0 0.0 0.0
#### Color-map plot of the LW in the BZ (2D systems)
In bidimensional materials it can be interesting to plot the linewidth of a certain band over the entire Brillouin zone. In a 3D materials, it is more tricky to get a nice picture, the possibility to automatically compute a 2D slice of a 3D BZ may be added in the future, if there is request.
&lwinput
calculation = 'lw full'
prefix="lw_2d"
file_mat2 = '../../1l.FILDYN/mat2R.4.vac.nozeu'
file_mat3 = '../../1l.FILD3DYN/mat3R.xxx_asr_sparse'
outdir = './'
asr2 = 'spread'
nconf = 1
nk = 20,20,1
sort_shifted_freq = .false.
/
CONFIGS
1.0 300
QPOINTS bz
50 50 1
You can than plot the resulting file with a gnuplot command like this (you will have to tune the pointsize and of course select the correct band to plot):
p 'lw_2d.50x50x1@bz_T300_s10.out' u 3:4:12 w points palette pt 7 pointsize 1.7 not
This is an example from graphene (done using 128x128 BZ-centered points):
### d3_tk.x
#### Compute the SMA solution of the BTE
The following input file computes the thermal conductivity in the Single-Mode Approximation. This example uses a finer grid of 24x24x24 q-points to compute the phonon lifetime on a grid of 12x12x12 points, which is integrated to compute the thermal conductivity. Furthermore, the natural isotopic distribution of Silicon is used.
&tkinput
calculation = 'sma'
prefix="tk"
file_mat2 = './mat2R'
file_mat3 = './FILD3DYN/mat3R.asr.sparse'
outdir = './'
asr2 = 'simple'
nconf = 1
nk = 12,12,12
nk_in = 24,24,24
casimir_scattering=.false.
isotopic_disorder =.true.
/
CONFIGS
5.0 10
ISOTOPES
Si natural
#### Compute the exact solution of the BTE
The following input file computes the thermal conductivity solving the BTE by functional minimization. This example also includes border scattering on grains of 1 micrometer average size.
&tkinput
calculation = 'cgp'
prefix="tk"
file_mat2 = './mat2R'
file_mat3 = './FILD3DYN/mat3R.asr.sparse'
outdir = './'
asr2 = 'simple'
nconf = 9
nk = 24,24,24
niter_max = 100
thr_tk = 1.d-4
casimir_scattering=.true.
casimir_length_mu = 1.0
/
CONFIGS
5.0 10
      20
      50
      100
      200
      300
      500
      1000
      2000
## Bibliography
A list of essential bibliographic references follows. When using this code you are not required to cite all of these work, however the authors would greatly appreciate if you cited references 1-4 where the theory and implementation of this work is described in detail.
In particular ref. 1 describes the calculation of 3rd order dynamical matrices using DFPT, and the calculation of ph-ph linewidth; ref. 2 describes the iterative solution of the BTE. In ref. 9 the formula used to compute the phonon-phonon scattering is derived. See also refs. 10-14 for previous methods, and for the inclusion of isotopic and border scattering. Ref. 3 and 4 include important applications and analysis of the BTE exact solution. Reference 5 describes the calculation of phonon spectra functions and the combination of 3rd and 4th order. References 6-8 contain the foundation of the theory used.
1. L. Paulatto, F. Mauri, and M. Lazzeri, Phys. Rev. B 87, 214303 (2013).
2. G. Fugallo, M. Lazzeri, L. Paulatto, and F. Mauri, Phys. Rev. B 88, 045430 (2013).
3. A. Cepellotti, G. Fugallo, L. Paulatto, M. Lazzeri, F. Mauri, N. Marzari, Nature communications 6 (2015)
4. G. Fugallo, A. Cepellotti, L. Paulatto, M. Lazzeri, N. Marzari, F. Mauri, Nano letters 14 (11), 6109-6114 (2014)
5. Lorenzo Paulatto, Ion Errea, Matteo Calandra, and Francesco Mauri, Phys. Rev. B 91, 054304 (2015)
6. M. Calandra, M. Lazzeri, F. Mauri, Physica C 456, 38–44 (2007)
7. Michele Lazzeri and Stefano de Gironcoli, Phys. Rev. Lett. 81, 2096 (1998)
8. N. Bonini, M. Lazzeri, N. Marzari, and F. Mauri, Phys. Rev. Lett. 99, 176802 (2007)
9. J. Garg, N. Bonini, B. Kozinsky et al., Phys. Rev. Lett. 106, 045901 (2011)
10. Joseph Callaway, Phys. Rev. 113, 1046
11. M. Omini, A. Sparavigna, Il Nuovo Cimento, 19, 1537 (1997)
12. M. Omini and A. Sparavigna, Phys. Rev. B 53, 9064 (1996)
13. M. Omini, A. Sparavigna, Physica B: Condensed Matter 212, 101-112, (1995)
14. M. Omini and A. Sparavigna, Phys. Rev. B 61, 6677 (2000)
## Change Log
##### v 1.1.1
- D3 calculation of metallic systems has been improved, only full bands used for the Sternheimer equation: improved convergence.
- Added debug options to d3 and qq2rr, added documentation for tools.
- Added manual grid shift from input to thermal2 codes.
##### v 1.1.0
- The phonon HWHM was mistakenly used in the SMA and CGP calculations, instead of the FWHM, thanks to Francesco Macheda for reporting and helping with debugging.
- version of d3q.x prior to 1.1.0 would save the complex conjugate of the D3 matrix (there is some freedom in the definition) which would result in poor result for most grid sizes (1x1x1 and 2x2x2 are fine). Now qq2rr contains a workaround that detects this case and takes the CC of the input D3 matrices
- openmp parallelization of d3_asr3.x allows for much faster sum rule, good scalability tested up to 4 or 8 CPUs
- the local part of the XC functional was always assumed to be Perdew-Zunger, this causes no error for PZ functional, a tiny error for PBE functional, possibly large error for other functionals.
##### v 1.0.7
- nasty bug in d3_tk.x, CGP calculation, wrong prefactor! Many thanks to Erpan Arking for reporting and helping with the debug!
- added calculation of JDOS and RMS of atomic displacements to d3_r2q.x
- better treatment of LO-TO along paths, still a bit hacky but it removes the ugly discontinuity
- support for random grids improved (should work in SMA)
- new auxiliary code d3_recenter.x that can be used to manipulate force constants (experimental)
##### v 1.0.6
nasty bug in d3_qq2rr.x where the 3rd order matrix would not be read correctly has been fixed: PLEASE REGENERATE THE FORCE CONSTANT FILES!!
##### v 1.0.5
- tiny fix on the previous version (symmetrization removed for scattering modes as it is not necessary and does not respect detailed balance, i.e. possible funny results with small grids)
- fixed a bug when using MPI parallelism and isotopes (isotopes would be ignored on CPUs after the first one)
##### v 1.0.4
one important change: quantities (linewidth, self-energy, scattering matrices, velocities) pertaining to degenerate phonon modes are now averaged out. This prevents broken symmetry when doing thermal conductivity calculations.
##### v 1.0.3
- fixed a case where a function result was used in an openmp reduce clause, causing segmentation fault on some intel compilers
- removed a mention of a non-existing unused subroutine, causing some compilers to rightfully complain
- not using vdCos and vdSin with intel compiler made easier (remove -D__HASVTRIG from thermal2/Makefile)
- openmp no more enable by default (it was actually unintended )
##### v 1.0.2
fixed old style namelist in tutorial example input file (and fixed code to still read those)
##### v 1.0.1
- remove line from PROGRAM_sparse.f90 that prevented compilation (thanks S. Appalakondaiah for reporting)
- calculation of 3-body force constant now done in two passess (100x times faster)
- 3d order acoustic sum rule now imposed in-place (faster and much lower memory usage)
##### v 1.0
everything!